	AEROSPACE / STANDARD	AS5506/TBD
		Issued 2014-02 Draft
SAE Architecture Analysis and Design Language (AADL) Annex Volume TBD: / Annex TBD: Subsets Annex

RATIONALE
The purpose of this annex is to provide a way to specify the scope of a tool, of an analysis or a source code generator with the definition of a subset of AADL. These subsets can be used to compare the scopes of AADL tools and ease the building of tool-chains. This annex aims at increasing AADL tool interoperability and increasing the confidence of tools users.

This Architecture Analysis & Design Language (AADL) standard document was prepared by the SAE AS-2C Architecture Description Language Subcommittee, Embedded Computing Systems Committee, Aerospace Avionics Systems Division.

Introduction
Annex Document S Subset Modeling
1. Scope
1. The purpose of the Subset Modeling Annex is to enable the specification of restrictions and requirements upon the use of the AADL language. It also proposes a set of predefined modeling patterns for well known embedded system architecture modeling standards such as Ravenscar or ARINC653.
2. This annex defines a method for the specification of restrictions and requirements called AADL subsets. A subset specification is expressed using a domain specific language referred as AADL Subset Specification Language (ASSET). ASSET relies on the AADL meta-model. The language features defined in this annex enable specification of sets of restrictions and requirements upon the use of AADL as sets of cardinality constraints on the superset.
3. This annex also provides a library of standardized subsets. This library formalizes ways to model famous APIs and runtime modeling standards.
4. The purpose of AADL is to model computer based embedded systems, including their runtime architecture. An AADL model is a hierarchical set of components, enriched with properties and annexes specific clauses. An AADL model can be use for multiple purposes such as design, verification, analysis or code generation. For each of those purposes, there exists numerous AADL dedicated tools, mapping from AADL to existing tools and analysis approaches (UPPAAL, Petri nets, timed automata's, among others) or source code generators. Each tool often cover only one use for AADL. Ideally, a designer using AADL would create one model that would be processed by each and every tools of a tool-chain covering the design process, and refined along those activities. From a modeling perspective, the key issue is to guarantee the model is amenable to all those analyses. As a matter of fact, a scheduling analysis tool would accept only a given set of thread patterns. Security policy enforcement focuses on communication patterns and flow of information, whereas fault error modeling and analysis tools would consider other exchange mechanism for fault propagation. Hence one needs to focus on the concepts accepted by a tool or a theory. This creates an interoperability paradox: models must be tuned to abide to specific tool capabilities or accepted patterns, and not to implement system specific requirements.
5. A AADL subset aims at making explicit the set of AADL models that is accepted by a tool, and easing the implementation of an associated model validation tool. Thus a subset enables to determine early in advance whether an AADL model is compatible with an analysis or a tool, but also to compare power of expression of subsets accepted by tools and to detect situations where a tool erroneously accepts an AADL model despite the absence of crucial information for analysis.
6. The AADL Subset Modeling annex is composed of three parts: a method to specify and to document AADL subsets, a method for subsets comparison and a library of standard subsets.
7. This annex proposes a DSL called ASSET to specify subsets and the constraints used to model them. ASSET aims at providing means for the specification and comparison of subsets and code generation for tool assessing the compliance of an AADL model to a subset.
8. Those constraints could be modeled using the constraint annex. Yet, the power of expression of the constraint annex is wider than ASSET's one. Indeed, the comparison of subsets required a normalized form of their constraints. Thus, ASSET aims at providing as less syntax rules as possible. Doing so, we limit the number of potential definitions for a unique constraint, which eases their normalization. Finally, subsets expressed with ASSET can be transformed towards the constraint annex language. To sum up, the constraint annex can be considered as a code generation target of ASSET.
Concepts and Terminologies
1. An AADL subset explicit restrictions and requirements of a given use of the AADL language. Subsets are modeled as sets of constraints upon the use of the AADL meta-model. A subset is constituted of two parts: a documentation and a specification.
2. The goal of an AADL subset is to specify the scope of an intended use of the AADL language. The targeted users are AADL users that need to understand which restrictions and requirements their AADL model needs to fulfill. Thus, a subset needs to be readable and understandable by non-experts of the tool, or standard they want to use.
3. Any entity of the AADL meta-model is listed in the appendix C.3 and the standard version 2. This meta-model supports multiple inheritance.
4. The documentation of a subset is expressed using natural language and is inserted within the specification of a subset as comments.
5. A subset specification is a list of restrictions and requirements upon the use of the AADL language and its annexes expressed with ASSET and documented in natural language.
ASSET: a DSL for subset specification
1. ASSET is a domain specific language dedicated to the definition of AADL subset specifications.
2. To allow the specification of subsets in a concise and homogeneous way we developed a domain specific language (DSL in the sequel). An ASSET specification consists in the declaration of a subset by means of a name associated with all the constraints that an AADL model must meet to be considered as compliant with the subset.
3. A subset must be documented in natural language. The documentation is constituted of two parts: an identifier, a general description (the kind of analysis provided by a tool, or the characteristics of the described standard for instance) and an individual description of all constraints composing the subset.
4. The subset identifier must be unique.
5. There are no restrictions regarding the subset general description content. The description must be inserted to the subset as comments above the specification of the subset's constraints.
6. The constraints are named using a unique identifier and classified using the AADL entity they constrain. For instance, all constraints relative to properties of processor or to the features needs to be grouped those entities.
Syntax
subsetDef::= subset subsetIdentifier ( {constraintDef}+ )

constraintDef::= constraintIdentifier : constraintBody ;

constraintBody::=
 there must be cardinalityExpression setDef
| the category of setDef must be typeDef
| for all variableDeclaration in setDef : ( constraintBodyAux )

constraintBodyAux::=
 constraintBody
| the value of elementIdentifier must be valueOperator
| the value of elementIdentifier must be specified
| ( constraintBodyAux and constraintBodyAux )
| ( constraintBodyAux or constraintBodyAux )

cardinalityExpression::= cardinalityOp cardinalityNumber

cardinalityNumber::= <integer>

cardinalityOp::= enumeration (exactly, at most, at least)

setDef::=
typeDef
| ownerIdentifier typeDef
| ( setDef variableDeclaration such that constraintBodyAux )

valueOperator::=
 valueContent
| less than valueContent
| greater than valueContent

valueContent::=
 <integer>
| <real>
| <string>
| <identifier>
| the value of elementIdentifier

ownerIdentifier::= <identifier>.

simpleIdentifier::= <identifier>

typeDef::= <identifier>

subsetIdentifier::= <identifier>

elementIdentifier::= <identifier> | ownerIdentifier elementIdentifier

constraintIdentifier::= <identifier>
Naming Rules
1. subsetIdentifier and constraintIdentifier must be unique within the whole set of defined AADL subsets.
2. typeDef must refer to an entity of the AADL meta-model or an attribute of such entities.
3. variableDeclaration defines a variable within a constraint. Thus, it cannot be identical to the name of any entity of the AADL meta-model.
Legality Rules
1. Any elementidentifier referenced within the syntax rules constraintBodyAux must be define in a constraintBody containing it. This definition can be made using the For all or the setDef constructs.
2. A variableDeclaration must be unique within each constraintDef.
Semantics
1. A subset model delimits the scope of AADL models that are supported by a particular use, or compliant with a given standard.
2. A model is said compliant with a subset if it meets all the constraints specifying it.
3. Any constraint expressed using ASSET can be translated towards a cardinality constraint form upon the AADL meta-model elements. A cardinality constraint can be build using only the following five following constructs:
  1. A test on the equality between the value of an attribute/property e and a given value v or the value of two attributes/properties e1 and e2.
  2. A function returning the cardinality of a set S: ǁSǁ as an integer.
  3. A test on the comparison between two integers. The allowed comparison operators (referred as ops in the latter) are the following: <,>,=.
  4. A test on the type T of the entities of a set S: hasType(T,S).
  5. A query on a set of elements S returning a subset of the elements ei in S' contained in S and where every ei meets a given constraint C: S' = query(S,C).
  6. Operators on integer +, -, *, /, union (or) , intersection (and) and negation (not) of booleans are allowed.
  7. The function rule(BNF_element) means that the transformation for the ASSET construct BNF_element is defined in another semantic rule.
4. subsetDef specifies a subset using an identifier subsetIdentifier and a list of constraintdef.
5. Constraintdef specifies a constraint using an identifier contraintIdentifier and a contraint specification constraintBody.
6. There are two kinds of constraints that can be defined within a subset: global and local constraints.
  1. Global constraints forbid or require the presence or absence of a given AADL entity, or given subtype for all the entity of one given type. It can be the presence of one and only one processor, or the fact that any features must be a data access for instance.
  2. Local constraints forbid or require a particular value for a given AADL entity's attribute or consist in a constraint over the relationship between two AADL entities. It can be the value of the preemptivity of a processor or the fact that each shared data must be connected to at least two threads for instance.
7. Any constraint is defined using a constraintBody.
8. Global constraints are built using the two first constructs of constraintBody:
  1. there must be cardinalityExpression setDef.
  2. the category of setDef must be typeDef
  3. cardinalityExpression::= cardinalityOp cardinalityNumber compares the cardinality of the setDef following it using the operator cardinalityOp and the integer cardinalityNumber. There are three cardinality operator: at least, at most and exactly.
  4. there must be cardinalityExpression setDef is translated towards a cardinality constraint with the form: 'ǁrule(setDef)ǁ ops cardinalityNumber', where the operators ops (<=, >= and =) respectively match the cardinalityOperators at least, at most and exactly.
  5. the category of setDef must be typeDef is translated towards a cardianlity constraint with the form: 'hasType(typeDef,rule(setDef))'.
9. setDef specifies a set of AADL entities. It can either be:
  1. an AADL classifier typeDef, then it represents the set of all the AADL elements with the type typeDef.
  2. an attribute of an AADL element or an AADL classifer (separated by a '.') ownerIdentifier typedef, where ownerIdentifier is either a reference to a predefined variable or an AADL classifier.
  3. ( setDef variableDeclaration such that constraintBodyAux ) specifies the subset of a given set of elements setDef that are all compliant with a given constraint constraintBodyAux. VariableDeclaration is an accessor to any element of the compliant subset. It is translated towards its cardinality form as 'query(rule(setDef), rule(constraintBodyAux))'.
10. ConstraintBodyAux defines a constraint that has to be contained within another constraint. It can either be a constraintBody or one of the following:
  1. the requirement on the specification of a value for an attribute: the value of elementIdentifier must be specified. It is translated towards its cardinality form as: '(ǁelementIdentifierǁ>0)'.
  2. the requirement on the value of an attribute: the value of elementIdentifier must be valueOperator. valueOperator compares the value of the elementIdentifer preceding it with a given value valueContent. ValueContent is a value of any AADL basic type or a the value of an elementIdentifer. Its cardinality form is: '(elementIdentifier ops valueContent)', where ops (<, > or =) matches valueOperator.
  3. The union of two constraintBodyAux: ( constraintBodyAux or constraintBodyAux ).
  4. The intersection of two constraintBodyAux: ( constraintBodyAux and constraintBodyAux ).
  5. The translation of the union and the intersection towards the cardinality form consists in applying boolean operators on the booleans resulting in the evaluation of the two constraints.
11. The local constraints are built using the last construct of constraintBody: for all variableDeclaration in setDef : ( constraintBodyAux ).
  1. A local constraint restricts the cardinality of a relationship between several AADL elements. Thus, the setDef construct used here must be the one specifying a subset of a set using a constraintBodyAux. If not, the constraint is global and needs to be defined using there must be cardinalityExpression setDef.
  2. The equivalent cardinality form of this construct consists in verifying that the cardinality of elements of setDef that do not meet the constraint is null: 'ǁquery(rule(setDef), not( rule( constraintBodyAux )))ǁ = 0'.
Example: ASSET

Subset Marzhin (
--Marzhin is a simulation tool for AADL models. It is integrated to AADLInspector. The intention of this --subset is to ensure that an AADL model can be simulated with Marzhin 1.0. Its subset is composed of --twelve restrictions. The restrictions are related to three property sets: properties defined in the --AADL_Project property set, the ARINC653 property set and some properties and in the Cheddar Property --Set. They also restrict the use of the Behavior annex to a limited set of behavioral operators. The --restrictions for the Marzhin tool are describe below.

--Marzhin1 : There is only one Processor component
Marzhin1 : there must be exactly 1 Processor;

-- Marzhin2 : The property Actual_Processor_Binding must be specified
Marzhin2 : for all p in Processor : (the value of P.Actual_Processor_Binding must be specified);
-- Marzhin3 : For all processors, property Scheduling_Protocol must have the following values only :
POSIX_Fixed_Priority_Scheduling_Protocol, Rate_Monotonic_Protocol or Deadline_Monotonic_Protocol
Marzhin3 : for all p in Processor : ( ( ( the value of p.schedulingpolicy must be
Posix_Fixed_Priority_Scheduling_Protocol
or the value of p.schedulingpolicy must be Rate_Monotonic_Protocol )
or the value of p.schedulingpolicy must be Deadline_Monotonic_Protocol ) ) ;

-- Marzhin4 : The property Dispatch_Protocol must have one of the following values : Periodic,
Aperiodic, Sporadic, Timed, Hybrid, Background.
Marzhin4 : for all t in Thread : ( ((((( the value of t.Dispatch_Protocol must be Periodic
or the value of t.Dispatch_Protocol must be Aperiodic )
or the value of t.Dispatch_Protocol must be Sporadic )
or the value of t.Dispatch_Protocol must be Timed )
or the value of t.Dispatch_Protocol must be Hybrid )
or the value of t.Dispatch_Protocol must be Background )) ;
-- Marzhin5 : Properties must be one of the following : Dispatch_Protocol, Period, Deadline, Priority,
Compute_Execution_Time
Marzhin5 : for all t in Thread : (	for all p in t.Properties : ((((( the value of p.Name must be Dispatch_Protocol
or the value of p.Name must be Deadline )
or the value of p.Name must be Period )
or the value of p.Name must be Priority )
or the value of p.Name must be Compute_Execution_Time )));

-- Marzhin6 : Features must be one of the following : Event Port, Event Data Port, Provides Sub-
program Access, Requires Subprogram Access, Requires Data Access
Marzhin6 : for all f in feature : ((((( the category of f must be Event_Port
or the category of f must be Event_Data_Port)
or the category of f must be Provides_Subprogram_Access)
or the category of f must be Requires_Subprogram_Access)
or the category of f must be Requires_Data_Access));

-- Marzhin7 : Features Properties must be one of the following : Queue_Size, Dequeue_Protocol
Marzhin7 :	for all f in Feature : ( for all p in f.Property : (( the value of p.Name must be Queue_Size
or the value of p.Name must be Dequeue_Protocol )));

--Marzhin8 : Dequeue_Protocol must have one of the following values : OneItem or AllItems
Marhin8 : for all f in Feature : ( for all p in
( f.Property p2 such that the value of p2.Name must be Dequeue_Protocol ):
(( the value of p must be OneItem or the value of p must be AllItem )) );

-- Marzhin9 : The property Concurrency_Control_Protocol must be set to Priority_Ceiling_Protocol
Marzhin9 : for all s in Shared_Data :
( the value of s.Concurrency_Control_Protocol must be Priority_Ceiling_Protocol );
)

AADL subsets comparison method
1. Subsets comparison of two subsets is made through the comparison of each constraints they contain. There are four comparison operators: equivalence between two subsets, inclusion of a subset by another, incompatibility between two subsets, intersection of two subsets:
  1. A subset A and a subset B are equivalent if and only if A and B are specified by the same constraints. Equivalence between the subsets of two tools means that they are fully interoperable.
  2. A subset A is included in a subset B if for all constraint c_B specifying B, there exists a constraint cA specifying the subset A such that the respect of c_A implies the respect of c_B. Thus, any AADL model compliant with the subset A will be compliant with the subset B. The inclusion of a tool's subset in another tool's one means that the latter can handle all AADL models the first tool can handle.
  3. A subset A and a subset B are incompatible if there is a constraint c_B specifying B, there exists a constraint c_A specifying the subset A such that the respect of c_A implies the non-respect of c_B. Thus, any AADL model compliant to the subset A will not be compliant to the subset B. An incompatibility between two tools' subsets implies that the tools manipulate disjoint sets of AADL models and are not able to be part of the same tool-chain.
  4. The subset I is the intersection of a subset A and a subset B if for all constraint c_I specifying I, there exists a constraint c_AorB specifying the subset A or the subset B. Thus, the intersection of A and B is a subset of both of them. The subset of a tool-chain is the intersection of the subsets of all tools composing it.

example
List of predefined Subsets
Ravenscar (UBO)
ARINC653 (Etienne Borde ?)
Synchronous (Jean-Pierre Talpin ?)
HOOD-HRT (?)
DO178C (?)
MILS (?)
Any other ideas and/or volunteers ?